## Slide 1: PhD Updates
Syed Salman Ahmed
Prof. Dr.-Ing. André Borrmann. Dr. Yelda Turkan, Florian Noichl
TUM Georg Nemetschek Institute / Chair of Computing in Civil and Building Engineering
Technical University of Munich.

## Slide 2: Conference Abstract
“An Open-Source Multimodal Dataset Generation Framework for RC Slab Bridge”
3D Geometric models
Simulated Point Clouds
Natural language description
Code + Parametric information
Accepted

## Slide 3: Conference Abstract
For generating 3D geometric models
A Python-based repository with parametric information.
Use Helios + for simulation real point clouds
Use LLM APIs for chat-auto completion using parametric information
Future Step: BridgePointLLM

## Slide 4: Refining Model: Assumptions
There are many ways to categorize bridges based on geometry, utility, structure, and construction type.
We are mostly concerned with Reinforced Concrete Highway/Motorway bridges.

## Slide 5: Variations in bridge models
A modular code is written to produce variations.
This includes having some independent variables that are given to the code and some dependent variables that are computed.

## Slide 6
Deck Sizes
Number of lanes
Number of Spans
*
Span Length
Bridge length
*
Width of lane
Shoulder/sidewalks etc.
+
Girder Type
Box Girder
T-Girder
Bridge Width
Girder Depth
Span to Depth ratio
Number of beams/cells
Girder Geometry
Girders
Number of Piers
Pier Type
MultiColumn
HammerHead
Column-shape
Rectangular
Circular
Pier Cap Type
Prismatic
Railing geometry
Railing Length
Abutment Type
WingWall
Wingwall Geometry
Piers
Deck
Girder
Railing
Abutment
Bridge Clearance height

## Slide 7: Deck | Width
Richtlinien für die Anlage von Autobahnen FGSV
Road and Transportation Research Association
Notes: Deck Width ( number of lanes ).
Number of lanes: Random between 2 and 4
lane_width = 3.5
hard_shoulder = 3.0
hard_strip = 0.5
sidewalk = 1.5 if include_sidewalks else 0.0
Total_width = lanes * lane_width + 2 * (hard_shoulder + hard_strip)

## Slide 8: Deck | Span length and Span-to-depth ratio
Innovative-Bridge-Design-Handbook-Construction-Rehabilitation-and-Maintenance-1.pdf
Notes: Deck Width ( number of lanes ).
Number of lanes: Random between 2 and 4
lane_width = 3.5
hard_shoulder = 3.0
hard_strip = 0.5
sidewalk = 1.5 if include_sidewalks else 0.0
Total_width = lanes * lane_width + 2 * (hard_shoulder + hard_strip)

## Slide 9: Deck | Inner span-to-End Span Ratio )
Concrete Box Girder Bridges Guide - J Schlaich, H. Scheffer

## Slide 10: T Girder / Beam and Slab Girder
y
z
Innovative-Bridge-Design-Handbook-Construction-Rehabilitation-and-Maintenance-1.pdf

## Slide 11: T Girder | Beam and Slab Girder
y
z
Deck width = = lanes * lane_width + 2 * (hard_shoulder + hard_strip))
Girder Spacing = (3.5, 4.5)
Deck Thickness = 300 mm
Girder thickness = 500 mm
Girder depth = Effective span length / 18.0
Innovative-Bridge-Design-Handbook-Construction-Rehabilitation-and-Maintenance-1.pdf

## Slide 12: T Girder / Beam and Slab Girder
y
z
Girder Spacing = (3.5, 4.5)
Deck Thickness = 300 mm
Girder thickness = 500 mm
Girder depth = Effective span length / 18.0
Number of girder = width / 3.5
Innovative-Bridge-Design-Handbook-Construction-Rehabilitation-and-Maintenance-1.pdf
Deck width = = lanes * lane_width + 2 * (hard_shoulder + hard_strip))

## Slide 13: Box Girder
y
z
Innovative-Bridge-Design-Handbook-Construction-Rehabilitation-and-Maintenance-1.pdf

## Slide 14: Box Girder
y
z
Number of cells, Girder Depth, Cell web thickness

## Slide 15: Box Girder
y
z
Web thickness = 0.5
Top slab thickness = 250 mm
Bottom slab thickness = 150 mm
Box_height = 2 m
Number of cells, Girder Depth, Cell web thickness
Cell_ratio = depth_of_girder / total_width_m
Number of cells depends on cell ratio
Innovative-Bridge-Design-Handbook-Construction-Rehabilitation-and-Maintenance-1.pdf
Concrete Box Girder Bridges Guide - J Schlaich, H. Scheffer

## Slide 16: Box Girder
y
z
Cell ratio between 1/6 to 1/5 -> 1 cells
Cell ratio less than 1/6 -> 2 cells.
Innovative-Bridge-Design-Handbook-Construction-Rehabilitation-and-Maintenance-1.pdf
Concrete Box Girder Bridges Guide - J Schlaich, H. Scheffer

## Slide 17: Railings
x
z
Richtzeichnungen für Ingenieurbauten 2023

## Slide 18
x
z
Railing height = 1.0 m
Center-center distance = 2.5 m
0.07 thickness
We will assume that the railing post is 7cm square in xy plane

## Slide 19: Piers | Types
NS_2020_Design_Of_Bridge_Piers_And_Pier.pdf
Number of Piers
Pier Type
MultiColumn
HammerHead
Column-shape
Rectangular
Circular
Pier Cap Type
Prismatic

## Slide 20: Piers | Hammerhead
z
y
p3
p4
p5

## Slide 21: Abutment | Wing wall
Wing wall
x
y

## Slide 22: Final Models

## Slide 23: Final Models